## Slide 1
Project Grace
A compliant robot designed to climb a vertical pipe
The Design
Four motor arms extend from a central electronics plate. Paired accordion flexures and outer zig-zag springs allow controlled movement, while motor holders and braces carry loads where stiffness is needed. The frame is designed around a 22 mm pipe and printed in PETG.
Four N20 gearmotors drive four custom twin-tire wheels, providing eight rubber tyre contact bands. The custom wheel bodies retain the supplied rubber tyres and transfer motor torque through a D-shaped shaft bore.
Key Dimensions
Pipe diameter: 22 mm
V7 centre plate height: 108 mm
Arm length: 92 mm
CAD target wheel-hub spacing: 43.2 mm
N20 motor envelope: 45.7 × 15.23 × 11.82 mm
Motor cradle clear length: 47.7 mm
Custom wheel tyre-seat ledge diameter: 31.88 mm
Custom wheel width: 22 mm
D-shaft: 2.85 mm diameter, with CAD print clearance
The Powertrain
At the stated 25–45 W system draw, nominal current is approximately 1.7–3.0 A. Ideal runtime from full capacity is about 16 minutes at 25 W or 9 minutes at 45 W. With 80% of capacity treated as usable, the estimates become roughly 13 and 7 minutes. Real runtime will be lower or vary with motor load, voltage sag and conversion losses. Confirm that every powered component is rated for a 4S pack’s 16.8 V maximum.
The controller drives upward until the limit switch activates, pauses for 11 seconds, then descends to ultrasonic distance thresholds of 110 cm and 200 cm, with a 2-second pause at the intermediate point. Distance is sampled every 100 ms; three consecutive sensor failures during descent trigger a stop and fault indication.
The Material
PETG is the baseline because its balance of stiffness and ductility suits the flexures. PLA may be stiffer and less tolerant of repeated high-strain movement; ABS may behave differently and can warp during printing. Substituting material requires testing the spring response, wheel contact and fatigue.
The custom wheel reuses the N20 motor’s rubber tyres on twin 6.5 mm-wide seats. A continuous rim supports the tyres, while the five-spoke web connects the rim to the hub with less material. The D-shaped bore transfers motor torque, and a 2.5 mm boss offsets the wheel from the frame.